## Slide 1
40 mm across · 50 mm tall
design → print → battle
Spinning Top Battle
Your design. Your rules. Last one spinning wins.
Computer Science 6 • Tinkercad Codeblocks
Notes: The unit finale: a design challenge with no steps. Students design a battle top in Codeblocks, print it, and fight it. The rubric grades the design work, not the tournament result — say that early, it licenses risk-taking. Structure of the period: short physics talk, research plus notebook sketch (the ticket into Tinkercad), build, export. One period.

## Slide 2
No instructions this time
That's not a gap in the lab. That IS the lab.
What the unit gave you
Shapes and holes. Variables and math blocks. Loops for anything repeated. Copy for anything reused. Group, color, export. Three builds' worth of tools.
What today asks
Use any of it, in any combination, to design a top that spins long and hits hard. Research is encouraged. Copying a classmate isn't — a battle of identical tops is a coin flip.
Plan first: a labeled sketch with dimensions in your notebook is your ticket into Tinkercad.
Notes: Recap: bubble wand (variables, loops), fingerboard (reading builds, copy, fits) — the toolbox is full; today tests whether they can open it without a recipe. The sketch gate matters: engineers don't improvise in the expensive tool. Approve sketches at the desk — 15 seconds each, and it catches the size-limit violations before they're 20 minutes deep.

## Slide 3
What makes a top good at this?
Two jobs: spin a long time, and survive contact.
Weight out wide
A heavy rim (a flywheel) keeps spinning long after a skinny top wobbles out. Think merry-go-round, not pencil.
Ride low
A low center of weight is hard to tip. Tall tops look cool and fall over cool, too.
Mind the edge
The rim is what meets the other top. Smooth ring? Bumpy attack edges? That's a design choice with consequences.
One more part matters: the tip. A small, rounded point spins. A flat bottom sits.
Notes: Keep this Socratic — they can reason out most of it. Ask: where do you stand on a merry-go-round to make it hard to stop? (Outside edge — that's a flywheel.) Tall skinny or short wide to survive a shove? (Short wide.) Why does a sharp pencil spin worse than a top? (Friction and balance at the contact point.) Physics is on the team of whoever thinks about it first — the lab's own words.

## Slide 4
The hard limits
40 mm across · 50 mm tall
That's 20 mm of radius. Measure the finished, grouped model — not just the first shape.
A top too big for the printer battles no one.
Notes: Constraints slide — short and non-negotiable, straight from the lab's warning box. The trap: building AT the limit, then adding a feature that pokes past it. Teach 'measure early, measure grouped.' If your printer or slicer adds constraints beyond these, announce them now.

## Slide 5
Research, then commit
Good designers steal ideas. Great ones write down why.
Research (8 minutes)
Search “3D printed spinning top.” Look for: where designers put the weight, how wide the flywheel is, what the tip looks like. Collect ideas, not files.
Sketch (your ticket in)
In your notebook: your top from the side, labeled with dimensions in millimeters, and one arrow pointing at your battle feature with a note on what it does.
Sketch approved at the desk = blocks unlocked.
Notes: Research is clocked — eight minutes with the sketch as the exit ticket keeps browsing from becoming the period. The sketch requirements are deliberately light: side view, dimensions, one labeled feature. That labeled arrow IS the rubric's 4-row ('a feature you chose on purpose that you can explain'). Approve fast and generously; the gate is for commitment, not perfection.

## Slide 6
Your turn — predict the winner
Same size, same weight. Different design.
Round 1: where's the weight?
Top A carries its weight in a thick rim at the outside.
Top B carries the same weight packed around its center.
Which one spins longer? Why?
Round 2: the collision
Top C is tall and narrow. Top D is short and wide.
They collide at full spin.
Who's still standing? What decided it?
Answers: A — weight at the rim resists slowing (flywheel) · D — low and wide is hard to tip; tall means tippy
Notes: Notebooks, then thirty seconds of neighbor argument before the reveal — the arguing is the point. Both answers restate the physics slide as decisions, which is the move the whole period asks for: turn a principle into a feature. Then release: research, sketch, build. 'Understand your mission for today?'

## Slide 7
Design moves in Codeblocks
The toolbox, aimed at this problem.
Torus
an instant flywheel rim — wide, heavy, already round
Cone or Paraboloid
the tip — small contact, rounded point, upside-down
Variables
RimWidth, TipHeight... tune the design without rebuilding it
Loop + Rotate
spikes, fins, or ridges around the rim, evenly spaced for balance
Group Selection
one solid top at the end — the printer wants one piece
Notes: Suggestions, not steps — this is the last slide before they're on their own. The loop-for-spikes row rewards your strongest students: anything decorating the rim must be evenly spaced or the top wobbles, and a loop guarantees even spacing for free. Balance is the hidden reason symmetric designs win. Uneven = wobble = early death, which is also why 'stack random shapes' loses to 'plan.'

## Slide 8
Your mission
1
Design your top in Tinkercad Codeblocks — sketch first, blocks second.
2
Stay inside the limits: no more than 40 mm across, 50 mm tall.
3
Give it at least one battle feature you chose on purpose — and can explain.
4
Turn it in: your spinning top's .STL file, submitted for printing.
After the printer: the arena. After the arena: a new unit, new hardware.
Notes: Deliverable matches Turn It In exactly: the top's .STL submitted for printing. Rubric's 4: fits the limits, and has a battle feature the student chose on purpose and can explain — that's the cold-close question, verbatim. This closes the Codeblocks unit; the battle happens once prints are done. Tease the next unit generically — new hardware, same habit: build, test, tune.