## Slide 1
MOVEMENT 1 · MOVEMENT 2 · MOVEMENT 3 · … · MOVEMENT 507
1868 · 507 · 112 mm · 8 days
Mechanical Movement Project
One motion in. A different motion out.
High School Engineering • Autodesk Fusion
Notes: The four numbers: Henry T. Brown published his catalog in 1868, it has 507 movements, every one of ours mounts on a 112 mm square base, and Part I runs eight class days. Open 507movements.com on the projector before this slide and leave it up; the animations do the selling. What's different from the patent project: that was one part built from a drawing; this is several parts that move against each other, and every one of them has to survive a printer. Part I ends when the mechanism runs in Fusion. The next project prints it and hangs it on the wall.

## Slide 2
What counts as a mechanism
The input is what a person does. The output is what happens. They have to be different motions.
Input
A crank, knob, or lever.
One hand operates it.
Parts and joints
At least 3 moving parts.
At least 4 joints of 2 types.
Output
A slider, a wheel, a pawl.
A different kind of motion.
→
→
Input motion | Output motion | Mechanism?
Crank turns around | Slider goes back and forth | Yes
Lever rocks | Wheel clicks forward one tooth | Yes
Small gear turns | Big gear turns slower, the other way | Yes
Wheel turns | Wheel turns | No: same motion in and out
Notes: The one test everything else hangs on: one motion in, a different motion out. A wheel on an axle with a handle moves, and it's not a mechanism, because the output is the input. The slider-crank from the joints lab is the reference case: the crank goes around, the slider goes back and forth, three moving parts, revolute and slider joints. Ask: 'What was the input on the slider-crank? What was the output?' (The crank; the slider.) Then: 'Name the input and output on a bicycle.' (Pedals turn; the wheel turns. Same motion, but faster: the chain and sprockets change the speed, which counts.) Vocabulary on the slide: mechanism, input, output. The lab bolds them.

## Slide 3
The rules your movement has to pass
Check your pick against all five before you ask for approval. I will.
1
Converts motion
One hand-operated input, a different kind of motion at the output.
2
3+ moving parts
Parts that move relative to the base. The slider-crank had three.
3
4+ joints, 2+ types
Not counting rigid joints to the base. A gear pair counts as a type.
4
5 to 12 printed parts
Including the base. Two copies of one pin are one unique part.
5
One-handed input
Operable while the base hangs on a wall. Gravity pulls toward the floor.
Pick an animated one
Color thumbnails move. Gray ones are a 150-year-old engraving and a paragraph. Allowed, not recommended.
Notes: These are in a table in the lab, word for word. Walk them with the projector on the 507 site: click a color thumbnail, watch it, and count out loud: input, output, moving parts, joint types. Then click a trivial one and show why it fails. Rule 4's ceiling matters as much as its floor; a 30-part escapement is next semester. Rule 5 is the one nobody thinks about until the print hangs on the wall and the slider falls to the bottom of its slot. Approval is step 2 of the lab: they show you the page and point at the input, the output, and each moving part. Hold that line; a movement that fails a rule on day 4 is a restart.

## Slide 4
The base
Every mechanism in the class mounts on the same square, so they hang together as a set.
112 mm
112 mm
4 mm thick
 | Requirement
Size | 112 × 112 × 4 mm. You model it; it counts as a part.
Orientation | Vertical. Pick the top edge and stick with it.
Material removed | Fine: holes, slots, pockets. Through holes are fine.
The back face | Nothing stands proud of it. Flush is fine.
The edges | Nothing extends past them. Everything inside the square.
Print limits | The base is exempt from 2 h / 50 g. Nothing else is.
Notes: The base is a plate with holes in it. Everything that sticks out of it is a separate part. Why: an axle grown out of the base prints standing up, every layer line across the direction it gets pushed, and it snaps (Strength rule). A separate axle prints lying down and presses into a hole with a 0.1 mm gap. The back face rule and the edges rule are about the display: these hang flat against a wall, tiled edge to edge, so nothing may poke out the back or past the sides. Don't explain the wall; just hold the rule. The print-limits exemption is only for the base; a 112 mm plate is about the size of the limit by itself. Point at the Design Rules page for the limits and the Strength rule.

## Slide 5
Fits and joints
One row in your joint table for every place two parts touch. The fit decides the gap; the motion decides the joint.
The two parts… | Joint type | Fit | Gap per side
are pushed together once and never move (axle in the base, cap on an axle end) | Rigid | Press | 0.1 mm
go together by hand and stay put, but could come apart | Rigid | Close | 0.2 mm
turn on each other (a wheel on an axle) | Revolute | Free | 0.3 mm
slide on each other (a slider between rails) | Slider | Free | 0.3 mm
turn and slide | Cylindrical | Free | 0.3 mm
a pin that rides in a slot | Pin-Slot | Free | 0.3 mm
are gears that mesh | Motion Link (not a joint) | — | plugin backlash
Gap per side is an offset: a 6 mm axle turning in a hole gets a 6.6 mm hole. Pins and axles are at least 3 mm across.
Notes: This is the Fits rule from the Design Rules page, with a column added: which Fusion joint goes with each fit. The joint table in the notebook has these three columns on the right, filled from this table, so the model and the assembly agree before either exists. The trap is per side: 0.3 per side makes the hole 0.6 bigger across. Say it twice. Gears: two meshing gears don't get a joint between them; each gets a revolute joint to its own axle and a Motion Link ties the two joints together. The lab has a short gear section that points at the Spur Gear Plug-in page; don't sell gears, most movements don't need them. Ways to hold a part on without glue, since fasteners and glue are out: a head on the axle and a press-fit cap, a shoulder, a flange. Each one is a row in the joint table.

## Slide 6
Your turn — before lab
Two movements. Decide with a neighbor, then we check.
A
The slider-crank from the joints lab: base, axle, crank, two pins, connecting rod, slider.
How many moving parts? Which joint types? Does it pass?
B
A wheel with a handle on its rim, turning on an axle pressed into the base.
What's the input? What's the output? Does it pass?
A: 3 moving (crank, rod, slider); revolute + slider; passes. B: input turns, output turns; fails rule 1.
Notes: Give them a minute with a neighbor, then take answers. A: the crank, the connecting rod, and the slider move; the axle and pins are rigid to the parts they're pressed into. Revolute (crank on axle, rod on both pins) and slider (slider in the rails): two types, four joints that aren't rigid-to-base. Passes. B: a person turns the wheel, and the wheel turns. That's a wheel, not a mechanism; it fails the first rule no matter how nice the handle is. Add a second wheel of a different size touching it and now the output turns at a different speed, which passes. The answers are in small type at the bottom edge for you, not for them.

## Slide 7
Eight days
It's a plan, not a stopwatch. Check yourself against it at the end of every period.
Day | Where you should be by the end of it
1 | Movement approved. Notebook entry started: movement record, parts list, joint table. Project folder made.
2–4 | Base and every part modeled, one Part Design each, holes and pins sized from the joint table.
5 | Assembly built, joints named, mechanism runs when you drag the input.
6 | Fixes. Interference and Draft Analysis clean. Exceptions recorded.
7 | Drawings of every unique part on the NPA Drawing Template.
8 | Demonstrations.
Notes: Same table as the lab's Pacing box. Today is day 1, and Fusion stays closed until the notebook has the movement record, the parts list, and the joint table; step 7 makes the project folder and that's as far as day 1 goes. Days 2 through 4 are one row on purpose: how the modeling divides up depends on the movement, so the check-in question those days is 'how many rows of your parts list are done?' Day 6 exists because the assembly always exposes something. Day 7 is drawings, every unique part, on the NPA template; the wrong template is the default ASME sheet, and a drawing on it gets sent back. Day 8 is a one-minute demonstration each, in hat order.

## Slide 8
Your mission
Three things. Turn It In is the same list you'll be graded on.
1
Your project folder Movement <number> - <short name> in your Fusion student folder: a Parts folder with one Part Design per printed piece, and your Movement <number> assembly beside it. Saving is submitting.
2
Your notebook entry Mechanical Movement Project: movement record, parts list, joint table, exceptions table (or "None"), a screenshot of the running assembly with its named joints, and a PDF drawing of every unique part on the NPA Drawing Template.
3
Your one-minute demonstration, given in class on day eight.
Next project: print it, build it, and make it work on the wall.
Notes: Read the three items; they are the lab's Turn It In word for word. The notebook entry carries most of the evidence: four tables, a screenshot, and the drawing PDFs. The demonstration is one minute, Fusion on the screen, describing the movement the way the 507 site describes it. The next slide is the same list broken into ten checkable lines; the lab ends with it too. Understand your mission for today?

## Slide 9
The Short List
Everything boiled down. If every line is true, you're done.
✓
Movement approved before modeling
✓
Project folder with a Parts folder inside
✓
One Part Design per printed piece, all in Parts
✓
Base 112 × 112 × 4; nothing past the edges or the back
✓
Assembly beside Parts; only the base grounded
✓
Every joint named; input drives output; Interference empty
✓
Notebook entry: movement record, parts list, joint table, exceptions
✓
Screenshot of the running assembly with joint names
✓
PDF drawing of every unique part, NPA template
✓
One-minute demonstration on day eight
The same list closes the lab document. Use it on day 7.
Notes: This is the lab's closing section, The Short List, one line per deliverable with no explanation, because the explanations are all above it in the document. It's the day 7 self-check: before demonstrations, every line should be true. Leave this slide up while they start steps 1 through 7. Fusion stays closed until step 7.