## Slide 1
10 pixels · 1 ball · 0 luck required
spin → slow → stop
Roulette Wheel
Your first program on real hardware
Computer Science 6 • Circuit Playground Express
Notes: First lab of the Circuit Playground Express unit. Hook: casinos rig roulette with a green space so you lose a little more than half the time — we're building the fun part (the spinning wheel) with none of the losing-money part. Two days. Day 1: the board, the setup-then-loop structure, a ball that spins and slows. Day 2: the stop trick, tuning, challenges. Deck spans both days; stop after the prediction slide on Day 1.

## Slide 2
Meet the Circuit Playground Express
A tiny computer that runs one file: code.py.
10
NeoPixels
the ring of lights, numbered 0–9 — today's wheel
A·B
Buttons
two push buttons — they star in the challenges
USB
CIRCUITPY
save code.py to the drive — saving IS the run button
No CIRCUITPY drive? Suspect the cable — charge-only cables look identical and do nothing.
Notes: Hold a board up while talking — it's the size of a cookie and it IS a computer. Demo live: plug in, show the drive appearing, open code.py. The pixels are numbered 0 to 9 starting near the USB connector and going around. The cable line is hard-won wisdom: a third of 'my board is broken' reports are charge-only cables. Test cables, not boards.

## Slide 3
The illusion of motion
Nothing moves. Ten lights take turns.
A movie is still pictures shown fast. Your "ball" is the same trick: turn OFF the pixel at i, add one to i, turn ON the new pixel. Done fast enough, your eyes write the story of one light traveling.
The wrap-around
The last pixel is 9. If i climbs past it, put it back to 0:
if i > 9: i = 0
Same reason a clock goes from 12 back to 1.
one trip through the loop
pixel[i] = BLACK
i = i + 1
wrap if past 9
pixel[i] = WHITE
sleep(0.1)
Notes: The variable i is the whole machine: it remembers where the ball is. Walk the loop card twice out loud, once with i = 3 (easy) and once with i = 9 (the wrap case). Ask: what happens if we skip the 'turn off' line? (A trail of lit pixels — actually a nice-looking bug; someone will find it in lab and you can name it a comet.) The clock analogy is the one that sticks.

## Slide 4
Every program this unit, forever
setup
runs once — imports, colors, variables
while True:
runs forever — the animation lives here
Indentation decides which is which. Code below the loop, unindented, never runs at all.
The lab tells you which steps go where. Read that part.
Notes: The structural idea of the entire unit: setup once, loop forever. Every lab from here on says 'do this before the infinite loop' or 'inside the loop' — students who internalize this slide debug themselves. The amber line is the lab's own warning box: indentation is meaning in Python, not decoration. Most common Day 1 failure: loop code typed unindented below the loop, board does nothing, student blames board.

## Slide 5
Slowing down: a delay that grows
Real wheels lose speed. Ours gains wait.
The trick
Start: delay = 0.1
Each loop, wait that long, then make it bigger:
delay = delay + 0.1
Longer waits between moves reads as "the ball is slowing down."
Watch it happen
print(delay) sends the number to the Serial terminal every loop.
You can literally watch the wait grow: 0.2, 0.3, 0.4...
Printing values is how programmers see inside a running program.
Notes: A variable changing itself — delay = delay + 0.1 — deserves a beat; read it as 'new delay is old delay plus a little more.' The print is not decoration: it's their first debugging instrument, and Day 2's tuning slide depends on reading it. End of Day 1 lab: everyone's ball spins and slows... and never stops. That's the cliffhanger — collect stop-the-ball hypotheses at the wrap and confirm NOTHING until tomorrow.

## Slide 6
Your turn — before lab
Two predictions in your notebook.
The wrap
i is 9. The loop adds one, checks the wrap rule, then lights pixel i.
Which pixel lights up next — and what would happen without the wrap check?
The slowdown
delay starts at 0.1 and grows by 0.1 each loop.
How long is the wait after five trips through the loop?
Answers: pixel 0 — without the wrap, pixel 10 doesn't exist and the program crashes · 0.6 seconds after five trips
Notes: Notebooks, two minutes, neighbor-check, reveal. The wrap question rehearses the exact crash they'd otherwise meet in lab (index 10 out of range) — meeting it on paper first turns a frustration into an 'I knew that.' Then release to lab, steps 1–13. 'Understand your mission for today?' DAY 1 ENDS here: spin plus slowdown working, stop unsolved, hypotheses collected.

## Slide 7
The stop: skip, don't halt
The program never stops. The ball just stops being moved.
The continue trick
First thing inside the loop:
if delay > 1.5: continue
continue means "skip the rest, next lap." The loop still spins — it just stops doing the moving part.
Was your hypothesis close?
Most ideas from yesterday stop the PROGRAM. This stops the MOTION and keeps the program alive — ready for a button press.
Then tune the feel
delay = delay * 1.1 — grow by 10% instead of a fixed step
delay = 0.01 — start fast
if delay > 1: — settle sooner
Change one number at a time. Watch print(delay). Decide with your eyes.
Notes: DAY 2 OPENER. Start from their written hypotheses — name a couple of good ones aloud before revealing. The distinction to land: stopping the program vs. stopping the motion. The program must survive because the button challenge respins it — a dead program can't hear a button. Tuning is real engineering: one variable at a time, observe, decide. Challenges in order: red/green wheel (their first modulo), random stop, button respin.

## Slide 8
Your mission
1
Make a single white light travel the ring on its own — then slow down — then settle on one pixel.
2
Tune the feel until it acts like a real wheel, and take on the challenges: colors, random, button respin.
3
Turn it in: submit your code.py file from the CIRCUITPY drive.
Next lesson: the board has a speaker — and a speaker plus a list of numbers is a music box.
Notes: Deliverable matches Turn It In exactly: code.py, submitted from the CIRCUITPY drive that appears when the board is connected. Rubric's 4: spins, slows, settles, tuned values, at least one working challenge. Tease the tune lab: same board, new organ — the piezo buzzer — and their own choice of song.