## Slide 1
A4 = 440 Hz · middle C = 261.63 Hz
numbers → music
Playing a Tune
A speaker plus a list of numbers is a music box
Computer Science 6 • Circuit Playground Express
Notes: Two days. Day 1: what frequency is, one tone on the piezo buzzer, then a melody from a list and a for-loop — which plays the right notes with the wrong rhythm, and that's the cliffhanger. Day 2: tuples give every note its own duration, then the challenges (rest, encore, light show). Warn the neighboring classrooms; thirty buzzers hunting for a chorus carries. Deck spans both days; Day 1 stops after the dark range slide.

## Slide 2
Frequency: wiggles per second
Measured in Hertz (Hz). More wiggles, higher pitch.
Slow wiggles — low sound
A drum skin flapping back and forth you could almost count. Low frequency, low pitch. The bottom of the lab's table: A0, at 27.5 wiggles a second.
Fast wiggles — high sound
A whistle vibrating thousands of times a second. High frequency, high pitch. cp.play_tone(440, 1) makes the buzzer wiggle 440 times a second, for one second.
One line of code, one note: cp.play_tone(frequency, seconds, cp.SQUARE_WAVE)
Notes: Play the 440 Hz tone live on your own board — one second of A above middle C is the entire demo. Connect to the do-now: humming higher means your vocal cords wiggle faster. The tone-generator website linked in the lab lets students SEE a frequency change as they hear it; worth 30 seconds on the projector. Vocabulary: frequency, Hertz — both defined in the lab where they're used.

## Slide 3
Musical notes are just frequencies
Every note has a number. The lab has the whole table.
note | Hz
C4 (middle C) | 261.63
D4 | 293.66
E4 | 329.63
F4 | 349.23
G4 | 392.00
A4 (concert A) | 440.00
Name your numbers
C = 261.63
D = 293.66
E = 329.63
Define a variable per note you need, and your song reads like music instead of like a phone book.
Pick your song first. AI is allowed for finding the note names — the code stays yours (AIAS Level 2).
Notes: Two representations of the same thing: musicians say 'A4,' the buzzer needs 440. The variable layer translates — code that says G, A, G is readable and checkable against sheet music; code full of raw decimals is neither. The AI note is the lab's actual policy, worth stating because it's the unit's first Level 2: AI may name the notes of their chosen song; the program is theirs. Cap song-choosing at five minutes or it becomes the period.

## Slide 4
A song is a list. A loop plays it.
Twinkle, Twinkle — seven notes, three lines.
song = [C, C, G, G, A, A, G]
for note in song:
cp.play_tone(note, 0.5,
cp.SQUARE_WAVE)
Read it aloud
“For each note in the song: play it for half a second.”
The loop visits every item in the list, in order, and note holds the current one — same idea as i on the roulette wheel, but Python does the counting for you.
Play it. Right notes... but something is off. What's missing?
Notes: The for-loop is new (roulette used while True) — the reading-aloud trick makes it self-explanatory. Let students build and play their melody, then let the flaw surface on its own: every note lasts exactly half a second, so Twinkle Twinkle sounds like a robot marching. Don't fix it today. 'Right notes, wrong song — why?' is the Day 1 cold-close, and tuples are tomorrow's answer.

## Slide 5
Your buzzer's range
27.5 Hz → 13,289.75 Hz
A0 at the bottom of the lab's table, G#9 at the top — ten octaves of numbers.
A piano stops at 4,186. Your board does not care. It will try anything.
Notes: Short beat to end Day 1's instruction. The table in the lab covers ten octaves; someone will immediately try 13,289 Hz, which is the point — it sounds like an angry mosquito and now the class understands frequency viscerally. DAY 1 lab from here: single tone, pick a song, note variables, list, loop. Tomorrow: rhythm.

## Slide 6
Tuples: a note married to its time
Some notes are long, some short. Store them together.
(C, 0.5)
note, duration
Unpack it into two variables
note, time = (C, 0.5)
The first name takes the first item, the second takes the second. Now both are ordinary variables — one goes to the pitch, one to the length.
Why a tuple and not a list?
A tuple can't be changed after it's made — which is exactly right for facts that belong together, like a note and its length, or an R-G-B color. They travel as a pair and can't drift apart.
Notes: DAY 2 OPENER. Recap the cliffhanger: right notes, robot rhythm, because the program stores WHAT to play but not HOW LONG. The tuple is the fix — the do-now already asked them to guess what (E, 0.25) means. Unpack on the board by hand with real numbers before anyone codes. The song becomes a list of tuples: song = [(C, 0.5), (G, 0.25), ...] and the loop unpacks each item. Then challenges: REST at frequency 0, encore (for-loop inside while True), light show synced to notes.

## Slide 7
Your turn — before lab
Two predictions in your notebook.
Time the song
song = [(C, 0.5), (G, 0.25), (F, 0.25)]
How long does the whole song take to play? Which note sounds longest?
The swap bug
A classmate writes: time, note = (C, 0.5)
then plays play_tone(note, time).
What does the buzzer actually do?
Answers: 1.0 second total, C is longest · it plays a 0.5 Hz “tone” for 261 seconds — the variables landed backward
Notes: Notebooks, two minutes, neighbor-check, reveal. The right card is the fun one: unpacking order matters, and getting it backward plays durations as frequencies — a four-minute silence, in this case, since 0.5 Hz is below anything audible. Students who hit this bug in lab will recognize it from the slide. Then release: convert your song to tuples, then challenges. 'Understand your mission for today?'

## Slide 8
Your mission
1
Play one clean tone at a frequency you chose — then a whole melody from a list with a for-loop.
2
Give every note its own duration with (note, time) tuples, until a classmate could name the song.
3
Turn it in: submit your code.py file from the CIRCUITPY drive.
Next lesson: you design the light show — and functions let you name an effect and replay it anywhere.
Notes: Deliverable matches Turn It In exactly: code.py from the CIRCUITPY drive. Rubric's 4: a recognizable song, notes as named variables, melody as a list of tuples, one for-loop playing it. The 'classmate could name it' bar is the honest test — encourage the wrap-up performances. Tease the functions lab: the light-show challenge they may have started becomes the whole assignment, with names.