## Slide 1
press → release → wait
button → keystroke
Making an Input Device
Your board tells the computer it's a keyboard. The computer believes it.
Computer Science 6 • Circuit Playground Express
Notes: One period. The board introduces itself over USB as a keyboard and the computer takes it at its word — then button presses become keystrokes, and keystrokes become game controls. The gate: button A must send a single clean letter before any game is opened. The concept: the press-release-wait pattern, and why each of its three lines is load-bearing.

## Slide 2
What a keyboard actually is
Not the plastic. The messages.
What it sends
Two messages, forever: “key A went DOWN” and “key A came UP.” That's the whole language. The computer never sees fingers — only messages arriving over USB.
So anything that speaks it...
...IS a keyboard, as far as the computer cares.
keyboard = Keyboard(usb_hid.devices)
One line, and your board joins the club.
If you speak the protocol, you're a keyboard. The computer checks your grammar, not your ID.
Notes: The reframe of the day: 'keyboard' names a conversation, not an object. Every controller, drawing tablet, and barcode scanner plays this same trick over USB HID. Connect to the do-now inventory: each device they listed sends messages; today they build one. Setup lines (import, Keyboard object) go BEFORE the loop — the structure slide from roulette still rules everything.

## Slide 3
The pattern: press, release, wait
Three lines. Each one earns its keep.
keyboard.press(Keycode.A)
tells the computer: key down
keyboard.release_all()
tells the computer: key up — skip this and the key is down FOREVER
while cp.button_a: pass
waits for YOUR finger to leave — skip this and one press fires dozens
All three live inside if cp.button_a: — which lives inside the infinite loop.
Notes: Walk it as a story: finger down → press → release → and then the program stands at the door until the finger leaves. The wait loop is the subtle one — the infinite loop runs thousands of times a second, far faster than a human can let go of a button, so without the wait, one human press is dozens of program passes, each sending a fresh key. The next slide shows the crime scene.

## Slide 4
Without the wait loop
AAAAAAAAAAAAAAAAAAAAAAAA
one press. one human, ordinary press.
The loop checks the button thousands of times a second. Your finger is not that fast.
Also: your board types into whatever window has focus. Including your code. Click somewhere harmless first.
Notes: Do this live on the projector if you can stomach it — comment out the wait loop, press once, watch the screen fill. Instant, visceral comprehension. The amber footer is the lab's own warning box and it is not theoretical: the board will type the letter A into the student's own code.py the first time they test with the editor focused. Undo fixes it; the habit of clicking a harmless window first prevents it.

## Slide 5
Keycodes: pick your controls
The name maps what gets SENT, not which button you pressed.
The popular ones
Keycode.SPACE — jump, in most games
Keycode.UP_ARROW / DOWN / LEFT / RIGHT
Keycode.W A S D
Keycode.RETURN
The full list is linked in the lab.
Design for a real game
Geometry Dash wants SPACE. Drift Boss wants basically one key. Pick the game, THEN pick the keycodes — a controller is designed for something.
Button A sending Keycode.B is legal, confusing, and occasionally hilarious. Design on purpose.
Notes: The subtle naming trap: Keycode.A means 'send the letter A,' regardless of which physical button triggered it. Board button A sending Keycode.SPACE is normal controller design. Task order from the lab: button B joins with the same pattern, then both get remapped for a chosen game, then the combo task (a single press sending a timed sequence — jump AND attack) for the quick finishers. Games are the test bench, not the reward — say it once, mean it.

## Slide 6
Your turn — before lab
Two predictions in your notebook.
Count the letters
The wait loop is missing. You press button A firmly for one full second.
Roughly how many letters arrive: 1, about 5, or hundreds? What decides it?
Place the line
keyboard = Keyboard(usb_hid.devices)
Does this line go before the infinite loop or inside it? What goes wrong in the other spot?
Answers: hundreds — the loop's speed decides, not your finger · before the loop; inside, you rebuild the keyboard every pass until it errors
Notes: Notebooks, two minutes, reveal. Left card cements the dark slide with a number they choose themselves. Right card re-tests the unit's structural rule (setup once, loop forever) in a fresh context — the object creation belongs in setup. Then release: steps 1–6 to the single-letter checkpoint, and no games until it passes. 'Understand your mission for today?'

## Slide 7
Level up: one press, many keys
A combo button is just a sequence with good timing.
if cp.button_b:
keyboard.press(Keycode.UP_ARROW)
keyboard.release_all()
time.sleep(0.1)
keyboard.press(Keycode.X)
keyboard.release_all()
Tune the sleep to the game
Jump-then-attack only works if the game sees the jump FIRST. The sleep between presses is the timing — adjust it until the combo lands in your game.
Don't forget the wait-for-release at the end, or your combo machine-guns.
Notes: The stretch task from the lab, for students whose two buttons already work: one physical press emitting a timed sequence. The idea generalizes — macro keys and accessibility switches are exactly this. Tuning the sleep against a real game is legitimate testing work, not goofing off, as long as the notebook says what values they tried. The bottom line reprises the pattern: even a combo ends with waiting for the finger.

## Slide 8
Your mission
1
Button A sends a single letter — one press, one key, no machine-gunning.
2
Both buttons send keycodes you chose on purpose, and they control a real game.
3
Turn it in: submit your code.py file from the CIRCUITPY drive.
Next lesson: lose the buttons — you'll steer the mouse pointer by tilting the board.
Notes: Deliverable matches Turn It In exactly: code.py from the CIRCUITPY drive. Rubric's 4: both buttons mapped to a game with the full press-release-wait pattern on each. Cold-close: walk me through press, release, wait — what breaks if each line is missing? Tease the accelerometer lab: same USB trick, but the next input isn't a button — it's gravity.