## Slide 1
tilt_x · tilt_y · tilt_z
tilt → move
Acceleration as Input
Last week a keyboard. This week a mouse you steer by tilting.
Computer Science 6 • Circuit Playground Express
Notes: One period. The board becomes a USB mouse: A clicks left, B clicks right (the press-wait pattern from last lab, from memory), and the accelerometer's tilt readings — scaled by a multiplier — steer the pointer. The new idea is reading a SENSOR instead of a button: continuous numbers, not yes/no. Warn early: once tilt control works, the board fights students trying to edit their own code. Unplug or hold level to edit.

## Slide 2
The accelerometer
The sensor that knows which way you're holding it.
What it senses
Speeding up, slowing down, changing direction — and tilt. It reports three numbers, one per axis: x, y, and z.
Where you've met one
Your phone rotating the screen when you turn it. Step counters. Game controllers. Cars deciding to fire airbags. Same sensor, different jobs.
tilt_x, tilt_y, tilt_z = cp.acceleration — one line reads all three.
Notes: Connect to the do-now: they guessed how the phone knows it's sideways; this is the answer, and there's one on the board in their hands. The unpacking line is the tuple move from the music lab — three values arriving together, caught by three names. New category of input: buttons say yes or no; sensors say HOW MUCH. That difference is the whole lesson.

## Slide 3
Mouse mode: the clicks are reruns
Same USB trick, same button pattern. New vocabulary.
mouse = Mouse(usb_hid.devices)
if cp.button_a:
mouse.click(Mouse.LEFT_BUTTON)
while cp.button_a:
pass
You know this
Object created in setup. Button checked in the loop. Wait for the finger to leave.
Button B repeats it with RIGHT_BUTTON. Try writing both from memory before peeking at the lab.
Notes: Deliberate rerun: last lab's pattern with mouse.click in place of keyboard.press. Challenge students to write both buttons from memory first and check against the lab after — retrieval beats re-reading. If the pattern isn't in memory, the lab has the complete code; no shame, next lab it will be. The interesting new work is on the next slide.

## Slide 4
Tilt becomes motion: three decisions
Two lines of math you'll want to argue with.
× 2
the multiplier — sensitivity. Bigger is faster. This is the number you'll tune.
− (minus)
flips the x direction. Games call this “invert look.” Delete it and steering mirrors.
int( )
the mouse moves in whole pixels — no such thing as moving 3.7 pixels.
mouse_x = -int(tilt_x * 2) mouse_y = int(tilt_y * 2) mouse.move(x=mouse_x, y=mouse_y)
Every trip through the loop nudges the pointer. Tilt more, nudge more.
Notes: The three annotations are the lab's own commentary turned into a table. The multiplier is the day's tuning knob — 2 is the starting suggestion, not the answer; the rubric expects evidence it was adjusted for their game. The minus sign is a one-character design decision students can feel instantly. int() exists because the mouse protocol wants integers — floats throw an error that looks scarier than it is.

## Slide 5
A secret about this sensor
It isn't measuring tilt.
It's measuring gravity.
Gravity always pulls straight down. Tip the board, and gravity's pull shifts across the x and y axes —
the board does the geometry and calls it tilt.
Notes: The mind-blow beat; let it breathe. Ask first: the board is flat and perfectly still — is the accelerometer reading zero? No: z reads gravity, about 9.8, forever. That's HOW it knows which way down is. Flat board: gravity all on z, x and y near zero, pointer still. Tilted: some of gravity leaks into x or y, and that leak IS the tilt number. Falling would read zero on everything — do not verify this with school hardware.

## Slide 6
Your turn — before lab
Predict the pointer.
Turn the knobs
You change the multiplier from 2 to 5.
You also delete the minus sign.
What does each change do to the pointer?
The flat board
The board lies flat and still on the desk.
What is tilt_x, roughly? What is the pointer doing? And which axis is NOT near zero?
Answers: 5 = faster/more sensitive; no minus = x steering reverses · tilt_x ≈ 0, pointer parked, z holds gravity (≈ 9.8)
Notes: Notebooks, two minutes, reveal. The right card checks the gravity slide stuck — z is the giveaway answer. Then release to lab: clicks first (from memory if they can), then tilt, then tuning. Remind them about editing with a live tilt mouse: unplug or hold the board level, or the pointer drags their cursor mid-keystroke. 'Understand your mission for today?'

## Slide 7
Tune it for a game
The multiplier is a feel, and feels are tested, not guessed.
The test loop
Pick a mouse-driven game (3D games work well). Play 30 seconds. Too twitchy? Lower the multiplier. Too sluggish? Raise it. Repeat until your hands stop noticing the controls.
Then finish the design
Remap A and B to something USEFUL for your game. Note your final multiplier in your notebook — with one sentence on why that number won.
Trade boards with a neighbor at the wrap. Their hands will find flaws yours forgave.
Notes: Tuning is the lab's actual task list, elevated to a method: one variable, short test, judge, repeat — the same loop that tuned the roulette wheel's delay. The notebook note gives the rotation check-in something concrete to look for (a multiplier that isn't 2, plus a reason). The board swap at the wrap is peer feedback that costs zero setup and reliably improves second drafts.

## Slide 8
Your mission
1
Button A clicks like the left mouse button; button B clicks like the right.
2
Tilting the board moves the pointer — tuned until the speed feels right for a game you chose.
3
Turn it in: submit your code.py file from the CIRCUITPY drive.
Next lesson: same sensor, new job — a tilt alarm, field-tested on a balance beam.
Notes: Deliverable matches Turn It In exactly: code.py from the CIRCUITPY drive. Rubric's 4: both clicks working, tilt steering, and a multiplier tuned for a specific game on purpose — not a twitch, not a crawl. Tease the finale: the unit's last lab points this same sensor at a balance beam and asks one design question — how much tilt is too much?