## Slide 1
green = level · red = falling · 440 Hz = told you
sense → decide → alarm
Tilt Sensor
A balance alarm you'll tune on a real beam
Computer Science 6 • Circuit Playground Express
Notes: Unit finale, one period. Everything is a rerun except the logic: colors from roulette, tones from the music lab, acceleration from the mouse lab. The new material is the threshold (one number splitting 'fine' from 'alarm') and if/elif/else (exactly one branch runs). Then the field test: a balance beam and the question 'how much tilt is too much?' — answered with a number they choose and defend.

## Slide 2
The build, in one picture
Level: calm green. Tilted: the low side complains. Loudly.
LEVEL
all ten pixels green, alarm silent — the reassuring state
TILTED RIGHT
pixel 2 turns red on the low side, 440 Hz alarm on
TILTED LEFT
pixel 7 turns red on the low side, same alarm
Level out again, and everything goes green and quiet. That last part is a feature you must build.
Notes: Show the finished behavior first — payoff before parts. Why the LOW side turns red: it's a warning light marking where you're falling, like the wing light a pilot would want, not a scoreboard. The bottom line plants the day's hard question early: nothing goes quiet on its own; 'off' is an instruction somebody has to write. That's the dark slide, coming.

## Slide 3
The threshold: a line in the sand
One number decides what counts as “too far.”
5
THRESHOLD
The decision it powers
tilt past +5 → tilted right. Past −5 → tilted left. Between them → level.
Smoke detectors, fever thermometers, speed cameras — all one reading compared to one chosen number.
ALL-CAPS names are a programmer's promise: this value is set once in setup and never changed by the loop — only by you, the designer.
Notes: Thresholds turn a continuous sensor (how much?) into a decision (which case?). Connect to the do-now smoke detector: it doesn't shriek at toast because someone chose its number. The ALL-CAPS convention is worth ten seconds — it's why the lab writes THRESHOLD and not threshold, and they'll see the convention in every language they ever learn. The 5 is a starting point; the beam decides the real value later.

## Slide 4
if / elif / else: one door opens
Three branches. Exactly one runs, every single loop.
if tilt_x > THRESHOLD:
pixels[2] = RED
start_tone(440)
elif tilt_x < -THRESHOLD:
pixels[7] = RED
start_tone(440)
else:
stop_tone()
Walk a number through it
tilt_x = +7 → first door: right side red, alarm on.
tilt_x = −3 → past both doors to else: alarm off.
The minus sign on the elif does all the work for left tilts.
Before the check, every loop starts by filling the ring green — the reset that lets red ever turn off.
Notes: Walk the three test numbers (+7, −3, +2) on the board with hands as doors — elif means 'only checked if the first failed,' else means 'everything that got past both.' Two traps live here: writing the elif without the minus sign (alarm fires while level), and putting the green fill inside a branch instead of before the chain (red pixels stick forever, since nothing repaints them). The bottom line is that second trap, pre-defused.

## Slide 5
Who turns the alarm off?
start_tone(440) ...
start_tone starts a tone and walks away. It plays until something stops it.
stop_tone()
The else branch is the off switch. Forget it, and you've built a very small car alarm.
Notes: The day's most common bug gets its own dark slide because thirty boards making an unstoppable 440 Hz tone is a memorable way to learn it. start_tone differs from the music lab's play_tone: play_tone plays for a duration and stops itself; start_tone latches until stop_tone. Nothing in computing turns itself off out of politeness — 'off' is a state you must program. The else earning its keep is the slide's whole argument.

## Slide 6
Your turn — before lab
Run the chain in your head.
Trace two readings
THRESHOLD is 5.
tilt_x reads +7: which branch runs, which pixel is red, is the alarm on?
Then tilt_x reads −3: now what?
Design the beam
On the balance beam, THRESHOLD = 1 builds what kind of challenge? THRESHOLD = 20? Which direction is “stricter”?
Answers: +7 → right branch, pixel 2 red, alarm on; −3 → else, alarm off · 1 = impossible (constant alarm), 20 = unfailable; smaller is stricter
Notes: Notebooks, two minutes, reveal. The left card is the comprehension check on the chain. The right card is the design question the whole field test turns on: fairness is a number, and they get to choose it — but they'll have to defend the choice at the wrap. Then release to lab: setup, loop, chain, and the beam rotation once their alarm works at the desk. 'Understand your mission for today?'

## Slide 7
The field test
Code that works on a desk meets a beam that doesn't care.
On the beam
Hold the board flat, walk the beam, let the alarm referee your balance. Tune THRESHOLD between runs: challenging but fair is the spec. Note your final number — and your reasoning — in your notebook.
While you wait your turn
The whole-side challenge: make ALL the pixels on the low side turn red, not just one. You know everything you need — which pixel numbers live on each side is the only research.
A threshold tuned on a desk fails on a beam. Test where it will live.
Notes: Logistics slide. Stagger the beam during lab time — one beam, thirty students, plan the queue. The whole-side challenge keeps the waiting productive; pixels 0–4 line one side of the board and 5–9 the other, which they can discover by lighting pixels one at a time. The desk-vs-beam line is real engineering wisdom in one sentence: test in the environment, not the workshop. Wrap: defend your THRESHOLD aloud.

## Slide 8
Your mission
1
Green ring while the board is level; past the threshold, the low side turns red and the alarm sounds.
2
Leveling back out turns the alarm off — then tune THRESHOLD on the beam until it's challenging but fair.
3
Turn it in: submit your code.py file from the CIRCUITPY drive.
That's the unit: lights, music, USB tricks, and sensors. Next unit — new tools, same habit of building.
Notes: Deliverable matches Turn It In exactly: code.py from the CIRCUITPY drive. Rubric's 4: both tilt directions handled, silence on leveling, and a THRESHOLD the student tested and can defend. This closes the CPX unit — take thirty seconds to name the arc: they made a board blink, sing, type, point, and judge balance. The generic tease is honest: whatever the next unit's hardware is, the habit (build, test, tune, defend your numbers) transfers whole.