## Slide 1
01000010 01001001 01001110 01000001 01010010 01011001
0101
Binary Numbers
How computers count with just two digits
High School Computer Science • Intro Lesson
Notes: Welcome students. Today we crack the code behind every computer: binary. By the end of class you'll understand WHY computers use binary and be able to convert numbers between binary and decimal by hand. In lab you'll practice these conversions, and next lesson we build on binary to explore logic gates — the physical switches that make computation possible. Ask: does anyone know how many different digits a computer actually uses to store everything — photos, music, this slideshow?

## Slide 2
Why do computers use binary?
A computer is built from billions of tiny switches (transistors). A switch has exactly two reliable states:
0
OFF
no current • low voltage
1
ON
current flows • high voltage
Two states = base 2
Reliable — only two levels to tell apart, so noise rarely flips a bit.
Simple to build — a switch is cheap and fast.
Everything — numbers, text, images, sound — is stored as patterns of 0s and 1s.
Notes: Ten fingers is why WE use base 10, but a computer has no fingers — it has switches. Each transistor is either off or on. Because there are only two states, we represent them with two digits: 0 and 1. This is base 2. Emphasize reliability: distinguishing 'off vs on' is far more dependable at billions of operations per second than distinguishing ten different voltage levels would be. One binary digit = one 'bit'. Every file on their phone is ultimately just a huge pattern of these bits.

## Slide 3
First, a reminder: place value
You already use place value every day in base 10. Each column is worth ten times the one to its right.
100s
10²
2
= 200
10s
10¹
5
= 50
1s
10⁰
3
= 3
2 5 3
200 + 50 + 3 = 253
Notes: Before binary, make the familiar idea explicit. The number 253 isn't three separate digits — each digit is multiplied by its column's value. Rightmost column is ones (10 to the 0), next is tens (10 to the 1), then hundreds (10 to the 2). So 253 = 2x100 + 5x10 + 3x1. Key point to plant: the ONLY thing special about base 10 is that the multiplier is ten. Binary works exactly the same way — we just swap the multiplier to two.

## Slide 4
Binary place value: powers of 2
Same idea — but each column is worth TWO times the one to its right. Memorize these:
2⁷
128
2⁶
64
2⁵
32
2⁴
16
2³
8
2²
4
2¹
2
2⁰
1
Reading left to right, the columns double each step: 1, 2, 4, 8, 16, 32, 64, 128 …
8 columns = 8 bits = 1 byte, which can store any value from 0 to 255.
Notes: These eight values are the whole game — encourage students to memorize them by doubling: 1, 2, 4, 8, 16, 32, 64, 128. Just like decimal columns were powers of ten, binary columns are powers of two. A group of 8 bits is called a byte. With 8 bits the largest value is 128+64+32+16+8+4+2+1 = 255, and the smallest is 0, giving 256 possible patterns. This is why you see 255 everywhere in computing (e.g. color values 0-255).

## Slide 5
Binary → Decimal
Add up the place values wherever there is a 1.
128
1
128
64
0
—
32
1
32
16
1
16
8
0
—
4
1
4
2
0
—
1
1
1
Binary 10110101
128 + 32 + 16 + 4 + 1 = 181
Notes: Work this one live on the board with them. Line the binary number 10110101 under the place values. Wherever there's a 1, the column 'counts' — circle those. Wherever there's a 0, it contributes nothing. Add the active columns: 128 + 32 + 16 + 4 + 1 = 181. That's the whole method: binary to decimal is just addition. Have students check: the two rightmost bits are 0 and 1 → does the number end up odd or even? (Odd, because the 1s place is on.)

## Slide 6
Decimal → Binary
Subtraction method: fit the biggest power of 2 you can, then repeat with the remainder.
Convert 45 to binary
1
Does 32 fit in 45?
Yes → 45 − 32 = 13
0
Does 16 fit in 13?
No → keep 13
1
Does 8 fit in 13?
Yes → 13 − 8 = 5
1
Does 4 fit in 5?
Yes → 5 − 4 = 1
0
Does 2 fit in 1?
No → keep 1
1
Does 1 fit in 1?
Yes → 1 − 1 = 0
Result
101101
45 = 32 + 8 + 4 + 1
Check by adding it back!
Notes: Two common methods exist (repeated division by 2, and this subtraction method). Subtraction tends to click faster for beginners. Walk down from the largest power of 2 that fits. Ask each question out loud: 'does this power fit in what's left?' Yes → write a 1 and subtract; No → write a 0 and move on. Reading the bits top to bottom gives 101101. Always verify by converting back: 32+8+4+1 = 45. Stress the self-check habit — it catches almost every mistake.

## Slide 7
Your turn — before lab
Try these with the powers of 2: 128 64 32 16 8 4 2 1
Binary → Decimal
1.
1010
2.
110011
3.
11111111
Decimal → Binary
1.
6
2.
20
3.
100
Answers: 1010=10 110011=51 11111111=255 | 6=110 20=10100 100=1100100
Notes: Give students 3-4 minutes to attempt these individually, then compare with a neighbor. Circulate. The answers are on the slide (small, at the bottom) — reveal or cover as you prefer. Note 11111111 = 255 ties back to the 'one byte, 0-255' point from earlier. These same skills are what the lab will drill. Once everyone is comfortable converting, we're ready to see what computers DO with these 0s and 1s.

## Slide 8
Next up: Logic Gates
Now that a bit is either 0 or 1, what can we DO with it?
AND
1 only if BOTH inputs are 1
OR
1 if EITHER input is 1
NOT
flips the bit: 0↔1
Logic gates are the physical switches that turn binary into computation — arithmetic, decisions, memory.
See you in lab — bring your powers of 2!
Notes: Close by bridging to the next lesson. We can store 0s and 1s — but computing means combining and transforming them. Logic gates do exactly that: tiny circuits that take one or two bits in and produce a bit out. Preview the three fundamental gates: AND, OR, NOT. From just these, you can build addition, comparisons, and memory — everything a processor does. Tell students the lab today cements binary conversion; next class we wire up gates and build a truth table. Encourage them to memorize the powers of 2 before then.