## Slide 1
A B → LOCK
AND · OR
Logic Gates
Making decisions with electricity
High School Computer Science • Digital Logic
Notes: Hook: you've been hired to design the lock for a high-security door. Two switches, one light, and a rule that decides who gets in. By the end of class students will know what AND and OR gates do, and in lab they'll build both as electronic door locks in Antares. Bridge from last lesson: we can COUNT with two symbols; today we start DECIDING with them.

## Slide 2
The design problem: a two-key door
Two switches, one electric lock. You write the rule.
The lock opens when voltage reaches it — shown by a lit LED. Each key turns one switch. The wiring decides what combination of keys opens the door.
The locksmith doesn't decide who gets in.
The wiring does.
High security
Two employees must turn their keys at the same time. Both switches, or no door.
Convenience
Any single employee opens the door with either key. One switch is enough.
Notes: Frame both rules before naming any gate. Ask: bank vault — one key or two? Missile launch consoles famously take two simultaneous keys. Then the punchline: the rule isn't a policy in a binder, it's wiring. These two rules have names, and they're the first two logic gates.

## Slide 3
The AND gate
Output is 1 only when BOTH inputs are 1.
A | B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Two switches in a row — in series. Current has to get through the first AND the second. One open switch anywhere breaks the path.
A·B
Engineers write AND as multiplication: the output is A×B. It only comes out 1 when both factors are 1 — the times table agrees.
One row lights the LED. Three rows keep the door shut.
Notes: Read the table aloud row by row — model the habit of treating a truth table as the complete story. Highlighted row: both on, door opens. Series wiring is the physical implementation; don't give away the lab by drawing it, but 'in a row' is a fair nudge. The A·B notation ties to multiplication: anything times zero is zero. Ask: which single switch can open this door? (None.)

## Slide 4
The OR gate
Output is 1 when EITHER input is 1 — or both.
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Two switches side by side — in parallel. Current takes whichever path is closed. Only when both paths are open does the door stay shut.
A+B
Engineers write OR as addition: A+B. Careful — in logic, 1+1 is still 1. The output doesn't count how many inputs are on; it only asks whether any are.
Three rows light the LED. Only silence keeps it dark.
Notes: Contrast with AND: three highlighted rows now. The 1+1=1 point matters — next week XOR will disagree with OR on exactly that row, so plant the seed: 'notice OR says 1 when BOTH are on. Keep that row in mind.' Ask: which lock is more secure? Which is more convenient? Who should win, and who decides? (The engineer, on requirements — not the wiring's mood.)

## Slide 5
Truth tables: the complete spec
Every input combination, exactly one output each. No ambiguity.
A sentence like “it opens when both keys turn” can be argued with. A truth table can't — it answers every case before anyone asks.
2ⁿ
rows
for n inputs
4
rows today
2 inputs → 2²
Count the combinations in binary
00
01
10
11
The input column is just counting from 0 to 3 in binary — last lesson, wearing a lab coat. List the rows in this order every time and you'll never skip a case.
Notes: Why truth tables at all: they're the engineer's contract. Ask 'how many rows for two inputs — and why exactly four?' Then the callback: the A/B columns count 00, 01, 10, 11 — binary from last lesson. Three inputs would be 8 rows; that shows up in the final lab of the unit. Habit to sell: fill rows in counting order, predict BEFORE simulating.

## Slide 6
Meet Antares
Your circuit shop. Three parts today — then wires.
⚡
Power
Net folder
The voltage source. No power, no light — the most common missing part.
✖
Real Switch
Input folder
Your key. Click it in simulation to turn it, like a finger on a light switch.
●
LED
Output folder
The lock indicator. Lit means voltage arrived — the door is open.
Label your switches A and B with the Text tool — your screenshots should explain themselves.
Notes: Follow this slide with the live two-minute speed-run: new circuit, drop Power + Real Switch + LED, wire, simulate, flip. Narrate misclicks cheerfully — the message is that the tool is approachable and errors in simulation are free. Then hands off: the lab doc has the component lists and the naming (MyAND, MyOR).

## Slide 7
Your turn — before lab
Commit to a prediction. The simulator will grade it.
Predict the wiring
Two switches can sit in a row (series) or side by side (parallel). Which layout opens the door only when both keys turn — and why?
Argue it from the current's point of view.
Predict the tables
In your notebook, write both truth tables from the rules alone — before you build anything. Four rows each, inputs in counting order: 00, 01, 10, 11.
In how many rows do AND and OR disagree?
Answers: series · they disagree in rows 01 and 10 — two of the four.
Notes: Two or three minutes, individually, then compare with a neighbor. The disagreement question is the sharper one: AND and OR differ only in the mixed rows. Reveal or cover the small answer line as you prefer. Then release to lab — 'understand your mission for today?'

## Slide 8
Your mission
1
Build MyAND — the two-key, high-security door. Both switches or nothing.
2
Build MyOR — the either-key door. Label switches A and B in both circuits.
3
Complete both truth tables in your notebook — predicted first, then verified.
Next lesson: you are the power source — your finger flips the switch. Computers don’t have fingers.
Notes: Restate deliverables: two working circuits, two screenshots, two truth tables in the notebook. Rubric is printed at the bottom of the lab — a 4 means exact behavior, labels, tidy wiring, correct tables. Tease next lesson: transistors, the switch that electricity flips.