## Slide 1
S · G · D
0 → 1
The Transistor
A switch that electricity flips
High School Computer Science • Digital Logic
Notes: Bridge: last lab their finger did the computing — every switch flip was manual. Today the switches start flipping each other. Also on deck: encapsulation (turning a circuit into a reusable named part) and, by end of the two days, a third gate: NOT. This deck runs across both days; stop after the encapsulation slide on Day 1.

## Slide 2
The problem with your switches
MyAND works — as long as you provide the fingers.
In lab 20, the inputs were your mouse clicks. Fine for a demo; useless for a computer. A processor makes billions of decisions per second, and none of them can wait for a hand.
What we need: a switch another circuit can flip.
Then gates can drive gates
If a switch is controlled by voltage, then one gate’s output can operate the next gate’s inputs — and circuits chain into machines. That single idea is the rest of this unit.
Notes: Let the problem land before the part: ask 'what's wrong with the circuits you built last week?' Nothing — except the operator. The computer can't include your finger. The requirement, stated plainly: a switch flipped by an electrical signal instead of a hand. Then introduce its name.

## Slide 3
Anatomy of a transistor
Three pins. One rule.
S
Source
Where current arrives — connect toward the voltage source.
G
Gate
The control pin. Voltage here closes the switch. This is the “finger.”
D
Drain
Where current leaves — connect toward the LED or output.
The rule: voltage at G connects S to D. No voltage at G, no path.
In lab you’ll use the N-type transistor — not P-type. Check twice; they look like siblings and behave like opposites.
Notes: One rule, said three ways: voltage at the Gate closes the path from Source to Drain. The Gate is the finger. In the lab each old switch gets removed and replaced by an N-type transistor — S toward power, D toward the LED side, G waiting for a signal. Warn about P-type now and again in lab; it's the most common silent error and it inverts everything.

## Slide 4
How many switches make a computer?
≈20,000,000,000
transistors in the chip inside a modern phone
Your circuit today: 2
Same part. Same rule. Just more of them.
Notes: Scale beat — keep it short. Every one of those twenty billion is the same three-pin part they're about to place, following the same one rule. Nothing in the phone is smarter than that; there's just an unreasonable quantity of it. Optional aside: transistors switch billions of times per second, which is where clock speed (GHz) comes from.

## Slide 5
Encapsulation: name the box
Define the inputs and the output. Hide the wiring.
A
B
→
MyAND
→
O
Once the circuit has named Circuit Inputs and a Circuit Output, it becomes a component — a part you can drop into a bigger design without ever looking inside again.
You flip light switches all day without opening the wall. That’s encapsulation — trust the interface, ignore the guts.
Notes: This is the big vocabulary word of the unit: encapsulation. In Antares: Circuit Input components wired to the transistor G pins (named A and B via the Name property — the property, not a text label), and a Circuit Output where the LED was. Sell the payoff: next week they'll place whole MyAND gates the way they place switches today. DAY 1 STOPS HERE — students go build; the Z mystery will find them, and the wrap collects hypotheses without confirming any.

## Slide 6
The mystery of Z
Your output isn’t 1. It isn’t 0 either.
Z
floating
connected to nothing
0
driven low
connected to ground
The fix: a pull resistor
It gently ties the output to ground, so “no signal” reads as a definite 0. When the transistors do conduct, current takes the easier path to the output and wins.
Off and disconnected are different things. A computer needs every wire to answer the question.
Notes: DAY 2 OPENER. Connect to their own Day 1 observations and written hypotheses — quote a good one by name if you can. The distinction that matters: 0 is a definite answer (ground); Z is no answer at all (floating). The pull resistor guarantees an answer. In lab: Pull Resistor from the Net folder, placed just before the Circuit Output, junction trick with the option key is in the lab doc.

## Slide 7
The NOT gate
One input. One job: flip it.
A | O
0 | 1
1 | 0
Also called an inverter. Feed it a 0, get a 1. Feed it a 1, get a 0. It’s the smallest gate — and with AND and OR it completes your starter set.
The build, in one breath
A pull resistor set to pull HIGH holds the output at 1 — until voltage at A switches the transistor on and drains the output to ground. Input on, output off. The full recipe is in the lab.
Careful: this resistor pulls HIGH. Your gates’ resistors pull LOW.
Notes: Two-row truth table — have them predict it from the description before showing (cover the table or reveal after). Conceptual heart: the pull-HIGH resistor makes 1 the default, and the transistor's only power is to drag the output down. That inversion of responsibility is why NOT needs a different pull direction than AND/OR — the amber warning is the lab's most common error.

## Slide 8
Your mission
1
Replace every switch in MyAND and MyOR with an N-type transistor.
2
Encapsulate: named inputs A and B, a Circuit Output, and a pull resistor so it reads 0 — never Z.
3
Build MyNOT, predict its truth table, and verify it in simulation.
Next: gates made of gates — and a circuit that does arithmetic.
Notes: Deliverables: MyNOT truth table in the notebook, screenshots of all three circuits. Rubric's 4: named I/O, outputs that always read 0 or 1, verified NOT gate. Preview: with AND, OR, and NOT encapsulated, next lab builds XOR without touching a single transistor — that's the point of everything they did today.