## Slide 1
NOT · AND · OR
gates → gates
Compound Gates
XOR, and the circuit that adds
High School Computer Science • Digital Logic
Notes: Today's claim: you never have to touch a transistor again. AND, OR, and NOT are now sealed components, and new gates get built from them the way those were built from transistors. By end of the two days: a gate called XOR, and a circuit that genuinely adds two bits. Deck spans both days — Day 1 through the XOR slides, Day 2 opens at the binary-addition recap.

## Slide 2
The ladder so far
Each layer is built from the one below — then sealed.
voltage
high or low — the raw physics
transistor
a switch that voltage flips
gate
AND · OR · NOT — sealed last week
compound gate
today: gates wired from gates
The rule of the ladder: build with the layer below. Never reopen it.
Nobody wiring an XOR thinks about transistors, and nobody placing transistors thinks about electrons. Every layer earns you the right to forget the one beneath it.
Notes: The abstraction ladder — this unit's through-line, and the picture to keep returning to. Each rung was a lab. Point out the payoff of last week's encapsulation: because gates are sealed boxes with named pins, today's wiring is drag, drop, connect. Ask: what got sealed at each rung, and what did sealing it buy you?

## Slide 3
XOR: “or” the way people mean it
Exclusive OR — one or the other, not both.
“Soup or salad?” includes a hidden rule: pick one. Plain OR is fine with both; XOR is the gate that enforces the “not both.”
XOR in the wild: the hallway light
One bulb, a switch at each end of the hall. Flip either switch and the light changes. The bulb is on exactly when the two switches disagree — that’s XOR, and it’s wired into your house.
The rule
output 1 when
exactly one
input is 1
Notes: Give XOR a human anchor before the table: 'soup or salad' (not both), and the hallway three-way light — the bulb is on exactly when the switches disagree. 'Disagreement detector' is a fair nickname and pays off later: XOR is also how a computer compares bits for equality.

## Slide 4
XOR vs. OR: one row of daylight
Three rows agree. One doesn’t.
OR
A | B | A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
XOR
A | B | A⊕B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Both true: OR says 1. XOR says 0. That single disagreement is about to matter enormously.
Notes: The amber row is the whole slide: 1,1. Ask which rows differ before revealing the highlight — it's the seed planted back in the OR lesson. Why it matters 'enormously': hold the mystery; tomorrow's addition slide cashes it in (1+1 is where a sum needs a carry, and XOR quietly writes the 0). Day 1 lab starts after this slide: predict the XOR table in notebooks, then build MyXOR from their own components.

## Slide 5
Remember binary addition?
One column. Three cases. One of them overflows.
0+0 = 0
easy
0+1 = 1
still easy
1+1 = 10
zero, carry the one
The answer has two parts: what stays in the column (SUM), and what leaves for the next one (CARRY).
Notes: DAY 2 OPENER — follows the do-now (adding one column by hand). Lab 10 callback: 1+1 in binary is 10, zero-carry-the-one. Split the result into two named jobs: SUM (stays) and CARRY (leaves). Two jobs means two wires, and it means one gate won't be enough — which is exactly the setup for the next slide.

## Slide 6
The half adder
Two gates you already own, doing arithmetic.
SUM = A ⊕ B (XOR)
writes the digit that stays in this column
CARRY = A · B (AND)
raises a 1 only for the 1+1 case — the overflow
A | B | SUM | CARRY
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Check the amber row against 1+1=10.
Notes: The reveal, and it should feel earned: compare the SUM column to XOR's output column — identical. Compare CARRY to AND — identical. The 'disagreement' from yesterday's amber row was arithmetic all along: 1+1 writes 0 and carries 1. So the half adder is nothing new: one XOR for SUM, one AND for CARRY, both fed by the same A and B. The lab builds it in exactly that order — SUM pass first, test, then add the CARRY pass.

## Slide 7
Why only “half” an adder?
It adds two bits — but a column in the middle of a number gets three.
Add 19 + 27 by hand. In the tens column you added three things: 1, 2, and the carry that arrived from 9+7. Every column except the first must accept a carry in.
The half adder has no third input. It can start an addition, but it can’t continue one.
HA
in: A, B
out: SUM, CARRY
missing: carry IN
Notes: Name the limitation precisely — it's next lab's cliffhanger. Have students narrate adding 19+27 and catch themselves handling three values in the tens column. The half adder's interface (two in, two out) simply has no socket for the incoming carry. The wrap question writes itself: what can't your new circuit accept? Next lab: the full adder — and then a machine that adds real numbers.

## Slide 8
Your mission
1
Predict the XOR truth table in your notebook, then build MyXOR from your own NOT, AND, and OR gates.
2
Build HA in two passes: wire SUM and test it, then add CARRY and test again.
3
Verify every row — all four combinations, both outputs. The 1+1 row is where impostors get caught.
Next: the full adder — and four of them become a computer.
Notes: Deliverables: XOR and half-adder truth tables (predicted first) in the notebook, screenshots of MyXOR and HA. Rubric's 4 requires verification against complete, correct, predicted tables. The 1+1 warning is practical: a plain OR miswired as XOR passes three of four rows — only the both-true case exposes it.