## Slide 1
0111 + 0011 = 1010
HA → FA → ×4
A Useful Binary Computer
The full adder, and a machine that does real math
High School Computer Science • Digital Logic
Notes: Unit capstone, two days. Day 1: the full adder — a half adder that accepts a carry — built from two HAs and an OR. Day 2: chain four of them and add real 4-bit numbers, including the one that doesn't fit. The title isn't a joke; by tomorrow's bell their circuit performs actual arithmetic, and the ladder from voltage to computation is complete.

## Slide 2
Addition with carry
1
19
+27
───
46
In the tens column you added three things: 1 (the carry), then 1 and 2. Your half adder has sockets for two.
The upgrade, stated as an interface:
full adder: A + B + Cin → SUM, Cout
Notes: Same move as the XOR reveal: extract the algorithm from what students already do by hand. Every column past the first adds THREE bits. So the required part is defined by its interface — three in, two out — before anyone wires anything. That's engineering order: spec first, build second.

## Slide 3
The full adder: built, not invented
Two half adders and an OR gate.
1
First HA adds A + B.
2
Second HA adds that result + Cin → final SUM.
3
Either HA may carry — OR merges them into Cout.
Can both half adders carry at once? Work a row and see — it’s a good notebook argument.
A | B | Cin | SUM | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Predict all eight rows before you build. 1+1+1 is the row that humbles people.
Notes: No new parts — the FA is composed from two sealed HAs plus MyOR, which is the ladder doing its job. Eight rows because three inputs: 2³, the truth-table slide from lab 20 paying off. The 1+1+1 row (amber) totals 3, which is binary 11: SUM 1, Cout 1. The side question (can both HAs carry at once?) has answer no — worth a notebook argument, not a lecture. Day 1 lab: predict eight rows, build FA, verify every row.

## Slide 4
Ripple carry
Chain the columns the way your pencil does.
FA₀
A0 B0 → S0
→
FA₁
A1 B1 → S1
→
FA₂
A2 B2 → S2
→
FA₃
A3 B3 → S3
Each Cout feeds the next Cin — a carry born in column 0 can ripple through every column
The first column has no incoming carry — tie FA₀’s Cin to Ground. Left floating, it reads Z — lab 30 already taught you that mystery.
Notes: The chain is hand addition, mechanized: each column's carry-out feeds the next column's carry-in. 'Ripple carry' because a carry born in column 0 can propagate the whole width — have them trace 0001 + 1111 and watch it travel. The ground note is the lab's second-most-common bug and a straight callback to the Z lesson: floating means no answer, and the first Cin must be told 'zero,' not left to guess. Wiring order discipline: A0 to the TOP adder — the lab warns twice for a reason.

## Slide 5
Overflow: when the box is too small
1001 + 1001 = ?
9 + 9 = 18, which is 10010 — five bits. Your adder has four.
S = 0010
reads as 2 — wrong
Cout = 1
the truth-teller
Fixed-width numbers are a promise with a limit. Cout is the wire that admits it.
Notes: Overflow graduates from vocabulary (lab 10) to an event they can produce on demand. The sum bits alone LIE — they read 2 — and only Cout tells the truth. Real-world hooks: old car odometers rolling over, vintage game scores wrapping to zero, and real integer-overflow bugs in shipping software. AP CSP connection: DAT-1.B, consequences of fixed-width representation. This becomes test condition 3 in their test plan.

## Slide 6
Engineers don’t hope. They test.
Three conditions, chosen on purpose.
1
No carry anywhere
e.g. 0101 + 0010 — the plumbing works
2
At least one carry
e.g. 0011 + 0011 — the ripple works
3
Overflow
e.g. 1001 + 1001 — Cout tells the truth
Compute each expected sum by hand first and write it down. Evidence that checks itself — a screenshot of a wrong answer looks exactly like a screenshot of a right one until you know what to expect.
Notes: The test plan is the deliverable that makes this engineering instead of arts and crafts. One condition per case — an overflow case that also happens to be the only carry case proves less than two separate cases would. The by-hand expected sums are non-negotiable and the rubric pays for them: a confidently wrong adder (scrambled input order) produces beautiful screenshots. Students pick their own numbers; the examples here are defaults, not assignments.

## Slide 7
Your turn — design your tests
Before you wire anything today.
Condition 1 — no carry
Pick two 4-bit numbers whose columns never carry. Prove it by adding them by hand.
Condition 2 — carry
Pick a pair where at least one column carries. Mark which column, and where the carry lands.
Condition 3 — overflow
Pick a pair whose sum needs five bits. Write the true sum, then what S3–S0 will falsely read.
Your morning do-now already produced condition 3. Two to go.
Notes: Five quiet minutes in notebooks before any wiring — the plan exists before the machine does. Circulate and challenge weak cases: 'does your carry case overflow too? Then which condition does it prove?' Once plans are down, release to the build. The rest of the period is the 4-bit adder and evidence collection.

## Slide 8
The ladder, complete
voltage high / low
transistor a switch voltage flips
gate AND · OR · NOT
compound gate XOR · half adder
adder FA × 4 — real arithmetic
Inside every processor sits an ALU — an arithmetic logic unit — and inside it, this exact idea, wider and faster.
You didn’t draw a computer. You built one.
Turn in: eight-row truth table, test plan, and three screenshots — one per condition.
Notes: Close the unit with the students doing the closing: reconstruct the ladder aloud, bottom-up, one rung per volunteer. Then the zoom-out: a real ALU is this idea at 64 bits with cleverer carry handling — wider and faster, not different. Deliverables restated in the footer. If there's a minute left: 'we analyzed it to death, and you built it anyway.'